## Slide 1
Sélim Amrari
Master thesis
February, 2018
Supervisors :
Romain Le Gendre, Dr. Hugues Lemonnier, Benoit Soulard
LEADNC, IFREMER - New Caledonia
Prof. Dr. Alfred Johny Wüest Physics of Aquatic Systems Laboratory, EPFL - Switzerland
Remote-sensing and classification of benthic landscapes for satellite derived bathymetry
Notes: Hello,
Today I m going to make a presentation about my master thesis
It will be about remote-seen
Work achieved in New Caledonia with IFREMER
20 seconde

## Slide 2: Summary
Introduction
  Satellite derived bathymetry, motivation and background
  Physic principles in water surrounding
  Aims of the thesis
  Study site: South part of the new caledonian lagoon
Materials
Methods and results
  Workflow
  Image pre-processing
  Bottom type and water classification
  The number of clusters
  Empirical modeling
Discussion
Conclusion
Notes: Shortly lets resume the summary of the presentation
We begin with an introduction: why sdb, how sdb where
Then we ll have a short description of the meterial
We follow by a description the diff step of the methodo and theirs result
Lastly we ll have a disscussion and a final conclusion
30 seconde

## Slide 3: Satellite derived bathymetry, motivation and background
Bathymetry, a key variable
PRESENCE :
« PREssions sur les Ecosys- tèmes récifo-lagonaires de Nouvelle-CalédoniE »
Traditional bathymetric measurements:
  By echo-sounder at the surface
  Expensive
  Not achievable everywhere
Satellite derived bathymetry :
  Less accurate but…
  Large scale water depth retrieval
  High Resolution
  Maximum depth : 25 – 30 meters
Sate of the art SDB:
  Empirical modelling
  Semi-analytical modelling
  Machine-learning
  Classification
Notes: Why bathymetry.
It is a very important variable. For hyd d model it is taking part of the boudarie condition. For coral ecosystem also, it allow to estimate the vulnarability to storm event and global warming. Here in new it is very interesting as there is several pristine coral areas.
However SDB remain less accurate than traditional measurement which are made by echo-sounder and has a maximum deppth of 25 30 meter in optimal clear water condition. Howerver it offer large scale depth water retrieval at high resolution at a lower cost.
45 seconde
Firt of all why bathymetry
Knowing Bath -> primary necessity. It represent a part of boundarie condition for hydrodinamic model. This is why we need the bathy grid with the highest resolution possible. In addition in coral ecos, it is a very impo variable. Allows to estim vulnerab to storm event and to global warming. Lastly, Lagoon of New Caledonia contain gap in pristine areas.
Traditionnal, bathymetric measurements are made by echo-sounder, a type of sonar, either mono or multi-beam, measuring water depth from sea surface.

## Slide 4: Physic principles in water surrounding
Radiance
  recorded by the satellite sensor
  corresponds to a measure of the electromagnetic radiation flux emitted or reflected by a surface
  dependent on :
    The area of the source,
    The view and solid angles of the sensor,
    The wavelength
    The irradiance
Attenuation
  Come from the Absorption and the scattering
Notes: Recorded signal by satelite is called the radiance. Not only dependent on the observed surface different, from reflectance
Reflection : is made of two different king of process.
Attenuation occuring in water surrounding produced two primary components. Absorption, molecular process energy of radiation is absorbed by the mater. Scattering which is a change in direction of radiation. It strongly dependent on the wavelength of radiation. Charactherized by a attenutation coefficient dependent on the water optical properties
Why am I telling you that : 3 main factor of variation of the recorded signal occuring in water surrounding. Bottom type _> bottom reflectance. The depth, which increase the amount of attenuation along the pathway, water compound change the water attenuation coefficient

## Slide 5: Aims of the thesis
Evaluation of empirical modelling
Direct application on a specific multi-spectral sensor
  Discussion of technical issues and procedures
  Scale of resolution
Range of optimal depth prediction
Proposed an approach by classification
Notes: Let s now highlight the aim of this thesis.
Primary aims at evaluating empirical methods of bath retrieval.
This work is applied using data from a specific passive sensor Sentinel2 which has been chosen. It is then a direct application of empircal metods to this sensor. The issues and the applied procedure will be disscussed.
Scale of depth retrieval.
Range of optimal depth w can be predicted
Lastly, an approach based on an initial classification is proposed. As seen the sens sig is dependend on bottom reflec, depth and water optical pro. This approach aims a t isolate the variation of the signal drivent by depth in subdatasets of calibration of models.

## Slide 6: Study site: South part of the new caledonian lagoon
Offers a great number of in-situ measurements by echo-sounding
set around the biggest city of the island : Nouméa
An extent of about 2’597.1332 km2
Semi-open area with four major channels through the barrier reef

## Slide 7: Satellite sensor and Bathymetric dataset
Satellite sensor : Sentinel-2A
  Open data
  Multispectral ground resolution : 10 meters
  Additional blue band with shorter wavelength
  Sensor composed of several detectors, set on slightly different view angles
Bathymetric dataset
  Provided by the French national hydrographic service, SHOM,
  Represents 18’556’254 measurements
  Measured by by echo-sounder with an accuracy of +-2% of depth
  Only the measurements up to 30 meters are kept
  Adjusted depth following the tide
Notes: Opend data-> allows to repeat the procedure freely
10 meters : respond to the need of numerical model
Additionnal blue bands -> higher penetration ability

## Slide 8: Satellite sensor and Bathymetric dataset
Satellite sensor : Sentinel-2A
  Open data
  Multispectral ground resolution : 10 meters
  Additional blue band with shorter wavelength
  Sensor composed of several detectors, set on slightly different view angles
Bathymetric dataset
  Provided by the French national hydrographic service, SHOM,
  Represents 18’556’254 measurements
  Measured by by echo-sounder with an accuracy of +-2% of depth
  Only the measurements up to 30 meters are kept
Notes: Opend data-> allows to repeat the procedure freely
10 meters : respond to the need of numerical model
Additionnal blue bands -> higher penetration ability

## Slide 9: Satellite sensor and Bathymetric dataset
Satellite sensor : Sentinel-2A
  Open data
  Multispectral ground resolution : 10 meters
  Additional blue band with shorter wavelength
  Sensor composed of several detectors, set on slightly different view angles
Bathymetric dataset
  Provided by the French national hydrographic service, SHOM,
  Represents 18’556’254 measurements
  Measured by by echo-sounder with an accuracy of +-2% of depth
  Only the measurements up to 30 meters are kept
Notes: Opend data-> allows to repeat the procedure freely
10 meters : respond to the need of numerical model
Additionnal blue bands -> higher penetration ability

## Slide 10: Method and results : Workflow
Downscaling of 4 bands up to 10m
Image Pre-processing :
  Thresholding : empirically defined
  Glint Removal
Computation of DII and Hue as descriptors
Definition of the number of clusters :
  Analysis relying on Ward’s method for Hierarchical clustering
  Analysis relying on Silhouette index
Bottom type and water classification by K-means :
  Aims at minimizing within-clusters inertia :
Empirical models calibration
Notes: Here is a descrioption of the workflow of the motho
First of all, 4 bands set at a lower ground resolution have to be downscal
Then image is pre-processed individually on each detector footprint. Soil and Clouds are thresholded taking advantage of spectral signatur of nat surfaces.
Glint is removed with a methodo described later
Descriptor uncorrelated from deph have to be computed and suitable number of cluster have to be chosen for the classification
After the classification, depth models are calibrated for each classes.

## Slide 11: Method and results : Image pre-processing
Achieved on individually on detectors’ footprint
Sun Glint Removal :
methods of Hedley et al., 2004
Notes: The second preprocessing is the Glint R. Very import steps as it is aims at removing the visible disparities between the detectors footprints
The method proprosed by hedley in 2004 is used.
It consist in extracting a sample of area showing an evident range of glint and homogeneous underwater brightness such as above deep water. From this sample we are using the NIR band which has almost no penetration ability in water so no volume scattering. And we are establishing a relation between the glint of each pixel and the variation of the NIR infrared band.
It is why we are extracting it above deep area.
From this sample we are using the near infrared band. Indeed it has a realy low penetration ability in water so its variation is directly linked to the glint. A relation is then established bet nir and band to correct. The value of the pixel that we want to correct is simply reduced by the product of the the regression slope and the difference between its NIR value and the observed minimum NIR value in the sample.

## Slide 12: Method and results : Image pre-processing
Initial Image
Corrected Image

## Slide 13: Method and results : Computation of the descriptors
Depth Invariant Index
Hue from HSV transformation
  HSV space is commonly used for aerial image classification
  We made the assumption the Hue is less dependent on radiation attenuation than Red, Green, Blue, Value or Saturation
Notes: It consist in extracting a sample of area with homogeneous bottom type. By the comparison of the logarithm signal of two different band, we observe that every pixel are set on linear trends with similar slope, dependent on the water optical properties, and different shift dependent on bottom reflectance. This shift is then representing the depth invariant Index of the pixel.
The second type of descriptor is DII. It is based on the comparision of log radiance of two band.
The log radiance are substracted from volume scattering.
In homogeneous water optical properties it is possible to observe a specific setting of the pixel along lines representing bottom reflectance.
Which has the same oriantation whose slope depend on water opti properties.
Method consist in extracting a sample of the image with homogenous bottom in order to find this slope. It is acting as a rotation in the space form by the log radiance of the two bands. Once the slope is defined

## Slide 14: Method and results : Computation of the descriptors
Color image
Hue
DII from Green and Blue
Classification

## Slide 15: Method and results : Computation of the descriptors
DII from Green and Blue
Classification
Color image
Hue

## Slide 16: Method and results : Computation of the descriptors
DII from Green and Blue
Classification
Color image
Hue

## Slide 17: Method and results : Computation of the descriptors
DII from Green and Blue
Classification
Color image
Hue
Patterns known as “blue holes” described by canyons on the back of the reefs

## Slide 18: Method and results : The number of clusters
Without-cluster Inertia Loss

## Slide 19: Method and results : The number of clusters
Without-cluster Inertia Loss

## Slide 20: Method and results : The number of clusters
Average Silhouette score

## Slide 21: Method and results : The number of clusters
Average Silhouette score

## Slide 22: Method and results : K-means classification

## Slide 23: Method and results : Empirical modeling
Stumpf
  Relies on the wavelength dependency of the attenuation processes which assumes that ratios of signals undergo stronger variation with depth than with bottom reflectance variation
  Litterature :
    Should have stabler results with different bottom reflectance
    Induces additional noises leading to the need a higher ground resolution
Lyzenga
  Proposes to educe errors driven by variation of bottom reflectance with a linear combination of bands
  relies on the subtraction of the average deep water signal in order to get rid of the volume scattering.
  Litterature :
    In practice, stability and range of depth of the results is still influenced by variations of environmental parameters.
Assumes constant water optical properties

## Slide 24: Method and results : Empirical models calibration

## Slide 25: Method and results : Empirical models calibration
Lyzenga: 3 classes

## Slide 26: Method and results : Empirical models calibration
Lyzenga: 3 classes

## Slide 27: Method and results : Empirical models calibration
Lyzenga: 3 classes
Notes: Lyzenga 3

## Slide 28: Method and results : Empirical models calibration
Stumpf: 8 classes
Notes: Stumpf 8

## Slide 29: Method and results : Empirical models calibration

## Slide 30: Method and results : Empirical models
Lyzenga: 3 classes
Stumpf: 8 classes
Notes: Different range of depth prediction. In bays it tend to be limited to 10 meters
In uitoé Stumpf seems sligltly more limited

## Slide 31: Discussion
Spatial correlation of the errors :areas close to the coasts
A low level clustering, allows an improvement of the precision’s performance

## Slide 32: Discussion
Spatial correlation of the errors :areas close to the coasts
A low level clustering, allows an improvement of the precision’s performance
With a pre-processing achieved individually on detectors’ footpring, nothing seems to prevent the application of the empirical methods on a extended area.

## Slide 33: Discussion
Spatial correlation of the errors :areas close to the coasts
A low level clustering, allows an improvement of the precision’s performance
With a pre-processing achieved individually on detectors’ footpring, nothing seems to prevent the application of the empirical methods on a extended area.
Lyzenga’s model can be evaluated as slightly better, regarding the precision of the overall models.
Lyzenga has higher precision 9/15 times

## Slide 34: Conclusion
Achieved work
  Sentinel-2 demonstrated its ability to produce SDB
  An approach based on classification as initial has been tested
  Possibility to produce large scale results is shown
  Strong spatial correlation of the errors estimate, specifically close to the coast
Future work
  The insertion of negative log areas in the classification results and their prediction using Stumpf model
  Realization of in-situ measurments of bottom type in order to create DII
  The merging of Lyzenga’s and Stumpf’s descriptiors using penalization parameter
  The outliers removal before classification

## Slide 35: Conclusion
Thank you for your attention
This work has been achieved with the collaboration of :
IFERMER - LEAND NC, EPFL, SHOM

## Slide 36: Image pre-processing
Sun Glint Removal :
methods of Hedley et al., 2004
Achieved on individually on detectors’ footpring
Soil and Clouds thresholding
  Threshold chosen by quantile computation following
  estimation of the ratio of water surface
Notes: The second preprocessing is the Glint R. Very import steps as it is aims at removing the visible disparities between the detectors footprints
The method proprosed by hedley in 2004 is used.
It consist in extracting a sample of area showing an evident range of variation of glint but with homogeneous underwater brightness.
It is why we are extracting it above deep area.
From this sample we are using the near infrared band. Indeed it has a realy low penetration ability in water so its variation is directly linked to the glint. A relation is then established bet nir and band to correct. The value of the pixel that we want to correct is simply reduced by the product of the the regression slope and the difference between its NIR value and the observed minimum NIR value in the sample.

## Slide 37: Bottom type and water classification (1)
K-means classifier
  Aims at minimizing within-clusters inertia :
    Initialize K cluster centroids …,
    Iterate until convergence:
      Every observation is assigned to the closest cluster:
      Update the clusters’ centroid position :
Requires to define the number of clusters
Every descriptors are standardized previously standardized
Notes: Commonly used in image classification

## Slide 38: The number of clusters
Agglomerative hierarchical clustering
    Start with each observation as a cluster
    Until only one cluster remains:
      Find the closest pair of clusters.
      Merge them.
Ward’s method:
  Define a measure of distance between clusters
  aims at minimizing the within-clusters inertia
Allows to observe the change in Inertia
Silhouette index
  Define a measure of how well an observation fit in a cluster

## Slide 39: Bottom type and water classification (2)
Depth Invariant Index
Hue from HSV transformation
  HSV space is commonly used for aerial image classification
  HSV transformation from a usual Red, Green, Blue space
  to a space formed by three other values:
  The Hue, the value, the saturation
  We made the assumption the Hue is less dependent on radiation attenuation than Red, Green, Blue, Value or Saturation
Notes: The second type of descriptor is DII. It is based on the comparision of log radiance of two band.
The log radiance are substracted from volume scattering.
In homogeneous water optical properties it is possible to observe a specific setting of the pixel along lines representing bottom reflectance.
Which has the same oriantation whose slope depend on water opti properties.
Method consist in extracting a sample of the image with homogenous bottom in order to find this slope. It is acting as a rotation in the space form by the log radiance of the two bands. Once the slope is defined

## Slide 40: Physic principles in water surrounding
Radiance
  recorded by the satellite sensor
  corresponds to a measure of the electromagnetic radiation flux emitted or reflected by a surface
  dependent on :
    The area of the source,
    The view and solid angles of the sensor,
    The wavelength
    The irradiance
Reflection
  Diffuse or specular
Attenuation
  Come from the Absorption and the scattering
Notes: Rapidly I would like to describe some basic physic principle :
Radiance first a all is the recorded signal from satellite sesor. It is a measure of the electromagnetic radiation emitted or reflected by surfaces but it is not reflectance.
Reflection: I want you to know that there is two type of reflection: diffuse ref wich produce equal ref in every direction and spec ref which produce rel in a specific direction. Above water, ref is mixture of both with spectular reflection which is responsible for the glint
Attenuation in water surrounding which is composed of absorbation , a molecure processes and scattering a change in the radiation direction. Attenuation is strongly dependent on the wavelength and on the water optical properties
As a resume 3 main factors of variaiton of the recoreded signal : deepth as it make vary the amount of att along the pathway, bottom type as it as its own reflectance, and wateer optical propertie which make change the coef of attenuation.
Sensored radiance is composed of a radiance component reflected by the bottom and attenuated along the pathway but also on the volume scattering component which is radiance scattered multiple time and never reaching the botto. It is what we observed above deep water.
We can also add the glint.
2 minutes
Recorded signal by satelite is called the radiance. Not only dependent on the observed surface different, from reflectance
Reflection : is made of two different king of process.
Attenuation occuring in water surrounding produced two primary components. Absorption, molecular process energy of radiation is absorbed by the mater. Scattering which is a change in direction of radiation. It strongly dependent on the wavelength of radiation. Charactherized by a attenutation coefficient dependent on the water optical properties
Why am I telling you that : 3 main factor of variation of the recorded signal occuring in water surrounding. Bottom type _> bottom reflectance. The depth, which increase the amount of attenuation along the pathway, water compound change the water attenuation coefficient

## Slide 41: Physic principles in water surrounding
Radiance
  recorded by the satellite sensor
  corresponds to a measure of the electromagnetic radiation flux emitted or reflected by a surface
  dependent on :
    The area of the source,
    The view and solid angles of the sensor,
    The wavelength
    The irradiance
Attenuation
  Come from the Absorption and the scattering
Notes: Rapidly I would like to describe some basic physic principle :
Radiance first a all is the recorded signal from satellite sesor. It is a measure of the electromagnetic radiation emitted or reflected by surfaces but it is not reflectance.
Reflection: I want you to know that there is two type of reflection: diffuse ref wich produce equal ref in every direction and spec ref which produce rel in a specific direction. Above water, ref is mixture of both with spectular reflection which is responsible for the glint
Attenuation in water surrounding which is composed of absorbation , a molecure processes and scattering a change in the radiation direction. Attenuation is strongly dependent on the wavelength and on the water optical properties
As a resume 3 main factors of variaiton of the recoreded signal : deepth as it make vary the amount of att along the pathway, bottom type as it as its own reflectance, and wateer optical propertie which make change the coef of attenuation.
Sensored radiance is composed of a radiance component reflected by the bottom and attenuated along the pathway but also on the volume scattering component which is radiance scattered multiple time and never reaching the botto. It is what we observed above deep water.
We can also add the glint.
2 minutes
Recorded signal by satelite is called the radiance. Not only dependent on the observed surface different, from reflectance
Reflection : is made of two different king of process.
Attenuation occuring in water surrounding produced two primary components. Absorption, molecular process energy of radiation is absorbed by the mater. Scattering which is a change in direction of radiation. It strongly dependent on the wavelength of radiation. Charactherized by a attenutation coefficient dependent on the water optical properties
Why am I telling you that : 3 main factor of variation of the recorded signal occuring in water surrounding. Bottom type _> bottom reflectance. The depth, which increase the amount of attenuation along the pathway, water compound change the water attenuation coefficient